## Slide 1
⚡
Probabilistic Energy Demand Forecasting
Dominion (DOM) Region · Virginia / Washington DC · 2005–2025
XGBoost · LightGBM · LSTM (Quantile Regression)
Dawit Adane · ML-1 Course Project · 2026

## Slide 2
Agenda
01
Problem Statement & Motivation
02
Dataset & Region Overview
03
Exploratory Data Analysis
04
Feature Engineering & Models
05
Results & Model Comparison
06
Future Forecast & Live Demo

## Slide 3
Problem Statement
Why forecast energy demand?
Traditional forecasting gives a single number.
We need to know: how confident are we — and what is the plausible range?
Grid Operators
Must balance supply/demand in real time — under-forecast = blackouts, over-forecast = wasted generation
Utilities
Bid into electricity markets hours ahead — point forecasts lead to costly imbalance penalties
Planners
Capacity decisions made 5–10 years out require uncertainty ranges, not single numbers
Researchers
Quantify how climate extremes and data center growth will stress the grid

## Slide 4
Why Virginia / DC?
The world's largest data center hub
Dominion (DOM) covers the Richmond–Washington DC corridor,
home to the highest concentration of data centers on Earth.
▸ Loudoun County ("Data Center Alley") hosts ~70% of global internet traffic
▸ Amazon AWS, Microsoft Azure, Google, Meta all operate hyperscale facilities here
▸ These facilities run 24 / 7 — unlike residential demand, the load never fully drops
▸ Demand surged ~45% between 2020 and 2025, far exceeding national grid averages
+45%
Demand growth 2020–2025
~70%
Global internet traffic routed through
9,000+
MW floor demand (3 AM, weekends)
20 yrs
Historical data 2005 – 2025
⚡ This makes DOM a uniquely challenging and important forecasting problem — conventional seasonal patterns are overlaid with a structural upward shift in baseload.

## Slide 5
Dataset Overview
PJM Interconnection — Dominion (DOM) region
Data Sources
Kaggle Historical (2005–2018)
▸ DOM_hourly.csv — 122,112 rows
▸ Hourly MW readings for the DOM zone
PJM Metered Data (2018–2025)
▸ hrl_load_metered_YYYY.csv (8 files)
▸ Official PJM settlement-quality MW data
▸ Deduplicated & concatenated with Kaggle
Combined & cleaned: ~175,000 hourly observations
175,000+
Hourly observations
20 years
2005 – 2025
2005–2024
Training set
2025
Test set (unseen)
2026–2030
Future forecast horizon
21
Engineered features

## Slide 6
EDA: Demand Patterns
Systematic daily and seasonal cycles
Chart: Average Monthly Demand (MW)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Avg Demand (MW) | 13200 | 12700 | 11900 | 11200 | 11800 | 13100 | 14800 | 14600 | 12400 | 11600 | 12300 | 13600
Summer peak
Jul–Aug highest demand (air conditioning load)
Winter peak
Jan–Feb second highest (space heating)
Spring dip
Mar–May lowest demand (mild temperatures)
Dual seasonality
U-shaped temperature– demand relationship

## Slide 7
EDA: Rising Baseload Trend
Data center fingerprint in the demand data
Chart: Yearly Average Demand (MW) — 2005 to 2025
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Yearly Avg Demand (MW) | 10800 | 10900 | 11100 | 11300 | 11200 | 10600 | 10300 | 10100 | 10200 | 10400 | 10500 | 10600 | 10800 | 10800 | 10800 | 10900 | 10700 | 10700 | 10900 | 12300 | 13500
2005–2019: Flat / declining
Energy efficiency gains offset population + economic growth
2019–2020: Brief COVID dip
Commercial/industrial load drops during lockdowns
2020–2025: Surge (+45%)
Hyperscale data center buildout in Northern Virginia Amazon, Microsoft, Google, Meta — all expanding rapidly

## Slide 8
EDA: Weather & Demand Relationship
Temperature drives both heating and cooling loads
Temperature vs Demand (2023)
Open-Meteo archive API · Washington DC (38.89°N, 77.04°W)
Scatter: Hourly temperature (°F) vs demand (MW)
▸ Below ~55°F: demand rises as heating kicks in
▸ Above ~70°F: demand rises as A/C load increases
▸ 55–70°F is the 'comfort zone' — lowest demand
▸ Pearson correlation ≈ +0.31 (linear, masking U-shape)
⚡ Data center load is temperature-insensitive — it creates a raised floor (~9,000 MW) that is visible even at mild temperatures.
Chart: Monthly Demand vs Temperature (2023)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Avg Demand (MW) — 2023 | 13900 | 12800 | 11600 | 11100 | 11900 | 13200 | 15200 | 15000 | 12600 | 11400 | 12200 | 13800
🌡 Temperature trend (°F): 38→85→41 — peaks Jul/Aug matching demand peak

## Slide 9
Feature Engineering
21 features capturing time, calendar, and lag patterns
Time of Day
▸ hour (0–23)
▸ hour_sin, hour_cos
▸ (cyclical encoding)
Calendar
▸ dayofweek (0–6)
▸ month (1–12)
▸ quarter, dayofyear
▸ weekofyear
▸ is_weekend flag
▸ is_holiday flag
Lag Features
▸ lag_1h (previous hour)
▸ lag_24h (yesterday same hour)
▸ lag_168h (last week)
Rolling Stats
▸ roll_mean_24h (last 24h avg)
▸ roll_std_24h (last 24h σ)
▸ roll_mean_168h (last week avg)
▸ roll_std_168h (last week σ)
Cyclical encoding (sin/cos) ensures the model understands that hour 23 is adjacent to hour 0 — no ordinal jump at day boundaries.

## Slide 10
Probabilistic Forecasting
Prediction intervals — not just a single number
What is Quantile Regression?
▸ Train three separate models on Q10, Q50, Q90
▸ Q50 = median forecast (like MAE-minimizing)
▸ Q10 = lower bound (10% of actuals fall below)
▸ Q90 = upper bound (90% of actuals fall below)
▸ Q10–Q90 band = 80% prediction interval
Loss Function: Pinball Loss
For quantile q: L = (y − ŷ) × q if y ≥ ŷ = (ŷ − y) × (1−q) if y < ŷ
Why Intervals Matter
Coverage
We target 80% — the actual demand should fall inside the band 80% of the time
Width
Narrow = high confidence. Wide = high uncertainty (e.g. extreme weather)
Grid ops
Operators reserve spinning capacity based on the upper bound (Q90)
Risk mgmt
Utilities can quantify worst-case costs without overbuilding

## Slide 11
Three Models
Gradient boosting and deep learning for quantile forecasting
XGBoost
▸ Extreme Gradient Boosting
▸ Shallow trees, strong regularization
▸ Trained separately for Q10/Q50/Q90
▸ Fastest training & inference
▸ Baseline — well-established approach
LightGBM
▸ Light Gradient Boosting Machine
▸ Leaf-wise tree growth (faster than XGBoost)
▸ Histogram-based — handles large datasets well
▸ Deployed in Streamlit app for live forecast
▸ Powers the 5-year recursive forecast
LSTM
▸ Long Short-Term Memory Network
▸ Sliding window: 168 hours (1 week) of history
▸ 3-output head: Q10, Q50, Q90 simultaneously
▸ Captures long-range temporal dependencies
▸ Best MAE — most accurate model overall

## Slide 12
Train / Test Split
Time-based split — no data leakage
TRAIN 2005–2024 (20 years · ~153,000 observations)
TEST 2025
2005
2010
2015
2020
2025
2026+
Why 2025 as test year?
▸ 2025 data exists — used as true holdout
▸ Models never saw 2025 during training
▸ Evaluates generalization to unseen future
Why train through 2024?
▸ Earlier split would waste recent data
▸ Data center surge (2020–2025) is in train set
▸ Model learns the new higher baseload regime

## Slide 13
Model Performance Results
Full 2025 test set — 8,760 hourly observations
Model
MAE (MW)
Avg Pinball
Coverage %
Interval (MW)
XGBoost
224.3
73.0
79.6%
687
LightGBM
230.5
73.7
78.9%
698
LSTM
171.6
58.8
93.8%
822
★ LSTM achieves best MAE and pinball loss. Wider interval reflects higher coverage (93.8% vs 80% target).
Chart: MAE (MW) — lower is better
| XGBoost | LightGBM | LSTM
MAE (MW) | 224.3 | 230.5 | 171.6
Chart: Coverage % — higher is better
| XGBoost | LightGBM | LSTM
Coverage % | 79.6 | 78.9 | 93.8

## Slide 14
Prediction Intervals
80% confidence band around Q50 forecast
← The Streamlit app shows interactive plots like this for any selected week in 2025:
80% Prediction Interval (Q10 to Q90)
── Q50 Forecast (LightGBM/LSTM)
·· · Actual Demand
Winter week Jan 6–12
Sharp morning ramp; model tracks well
Summer peak Jul 7–13
Sustained afternoon plateau; wider intervals reflect A/C uncertainty
Holiday week Dec 17–25
Demand drop on Dec 25; holiday flag captures the drop

## Slide 15
Key Finding: Data Center Signature
A structural shift hidden in the demand curve
Average demand grew from ~10,700 MW (2019) to ~13,500 MW (2025) — a +26% structural shift
This is not seasonal variation. This is always-on compute load from data centers.
Flat 3AM load
~9,000 MW minimum even at 3 AM on holiday weekends — residential + commercial demand alone cannot explain this baseline.
Smaller weekend dip
Traditional grids see 15–25% demand drop on weekends. DOM's weekend dip is shrinking — data centers don't take Sundays off.
Higher low-temperature floor
Even in mild spring weather (55°F), DOM demand rarely drops below 10,000 MW. Historical data showed 8,500 MW lows — the floor has risen.
Forecast implication
Models trained only on pre-2020 data severely under-forecast present demand. Training through 2024 ensures the model has learned the new regime.

## Slide 16
Future Forecast: 2026–2030
Recursive LightGBM — 43,824 hourly steps
Recursive Forecasting
▸ Seed with last 200 known hourly values (Dec 2025)
▸ Predict step t+1 using lag features from history
▸ Append Q50 prediction to history buffer
▸ Repeat for 43,824 steps (2026-01-01 to 2030-12-31)
▸ Prediction intervals preserved throughout (Q10/Q90)
Pre-generated & cached as parquet:
▸ Loads instantly on every app start
▸ Deterministic — same result each time
▸ ~1.5 MB file in the repo (Git LFS)
Projected Ranges
Peak Q50 (summer)
~20,600 MW
Min Q50 (spring AM)
~9,600 MW
Avg uncertainty band
~2,000 MW
Horizon
1,825 days
⚠ Long-horizon caveats:
Intervals widen due to cumulative lag uncertainty. Seasonal structure is reliable; absolute MW levels are projections.

## Slide 17
Live Demo — Streamlit App
Interactive probabilistic forecast explorer
⚡ https://energy-demand-forecasting-ml.streamlit.app
📊 Model Evaluation
Select any week in 2025, choose LightGBM / LSTM / XGBoost, view forecast vs actual with 80% intervals
🏆 Model Comparison
Side-by-side metrics table and bar charts; summer peak week comparison for both models
🔍 EDA
Hourly / daily / monthly / yearly demand patterns; weather-demand relationship charts (2023 DC data)
🔮 Future Forecast
Date range picker for 2026–2030 with quick select; recursive LightGBM Q10/Q50/Q90 bands
ℹ️ About
Project overview, dataset details, model descriptions, performance table, and key findings
All predictions pre-cached · Loads in < 2 seconds · No API keys required

## Slide 18
Conclusions & Key Takeaways
Probabilistic > point forecasting
Quantile regression provides actionable uncertainty ranges — critical for grid operations
LSTM wins on accuracy
171.6 MW MAE vs 224+ for tree models; 1-week sliding window captures temporal dependencies
LightGBM wins on speed
Instant inference, recursive 5-year capability, ideal for production deployment
Data centers are reshaping the grid
The +45% demand surge in DOM is a fingerprint of hyperscale growth — not seasonal noise
Feature engineering is critical
Lag features, rolling statistics, cyclical encoding give models the temporal context they need
Future Work
▸ Add weather forecasts as live features
▸ Transformer / Temporal Fusion network
▸ Incorporate data center capacity data
▸ Real-time PJM API integration
▸ Multi-region forecast (PJM-wide)
▸ Anomaly detection for extreme events
Thank you · Dawit Adane · ML-1 Course Project · 2026
⚡ energy-demand-forecasting-ml.streamlit.app